## Slide 1
专业英语
Specialized English
PPT： 李聪
翻译： 谭良静
演讲： 卢显杰

## Slide 2
目录
CHAPTER 4
Methods of Solution

## Slide 3
CHAPTER 4
3
Methods of Solution
4-3 Methods of Solution
Iterative techniques will probably remain the only way to solve the general load-flow problem. The types of iterative techniques and the variations on them are numerous. Each type seems to have some particular advantage.
迭代技术可能仍然是解决一般潮流问题的唯一方法。迭代技术的类型及其变化是很多的。每种类型似乎都有一些特殊的优势。
Iterative techniques 迭代技术
remain 依然
types of 各种类型
Variations 变化，变动

## Slide 4
CHAPTER 4
Methods of Solution
Although some iterative techniques seem to be much preferred over others, their effectiveness is sometimes a function of the characteristics of the particular power system. For this reason it is almost impossible to provide an unbiased test for their effectiveness.
4
虽然有些迭代技术似乎比其他技术更受欢迎，但它们的有效性有时是特定电力系统特性的函数。因此，几乎不可能对其有效性进行公正的测试。
effectiveness 有效性 function 函数
characteristics 特性，特征
power system 电力系统，动力系统
unbiased test 公正的测试，无偏检验

## Slide 5
CHAPTER 4
Methods of Solution
The difficulties and the importance of the load-flow problem have fascinated mathematicians and engineers throughout the world for a number of yeas.
5
多年来，潮流问题的困难和重要性一直吸引着世界各地的数学家和工程师。
load-flow problem 负荷流动问题；潮流问题
fascinated 着迷的; 被深深吸引的
throughout the world 全世界

## Slide 6
CHAPTER 4
Methods of Solution
Many people have devoted a large proportion of their professional life to the solution of the problem. It has received more attention than all the other power-system problems combined.
6
许多人在职业生涯中投入了很大一部分精力来解决这个问题。它比所有其它电力系统问题加起来更受关注。
devoted 献身于…; 致力于…
a large proportion of 一大部分
professional 职业的; 专业性的; 专业人士
Received 接到；收到
combined 结合的; 组合的

## Slide 7
CHAPTER 4
Methods of Solution
The amount of effort devoted to the problem has resulted in an enormous amount of technical publications. Readers interested in the many advancements in this field should study the past and current technical publications.
7
投入大量精力解决这个问题已经产生了大量的技术出版物。对这一领域的许多进步感兴趣的读者应该研究过去和现在的技术出版物。
devoted to 专心于
Resulted 导致；产生
Field 场；领域
the past and current 过去和现在

## Slide 8
CHAPTER 4
Methods of Solution
The brief introduction given here is only intended to define the most elementary portion of the problem to the reader. The more important and sophisticated techniques would be out of place in such a simple introduction.
8
这里给出的简短介绍仅用于向读者定义问题的最基本部分。更重要和更复杂的技术在这样一个简单的介绍中是不合适的。

## Slide 9
CHAPTER 4
Methods of Solution
The earliest load-flow method that came into general usage on digital computer was the Gauss-Seidel method. Although the Gauss-Seidel procedure is simpler and less demanding of computer capacity (such as memory), it does suffer from serious shortcomings, such as converging very slowly toward a solution for systems with a large number of buses and in some cases even failing to converge.
9
最早出现在数字计算机上的潮流计算方法是高斯-赛德尔法。虽然高斯-赛德尔程序更简单，对计算机容量（如内存）的要求也更低，但它确实存在严重的缺点，例如，对于具有大量总线的系统，它的收敛速度非常慢，在某些情况下甚至无法收敛。

## Slide 10
CHAPTER 4
Methods of Solution
Huge advances have recently occurred in the technology of digital computers, especially with regard to memory capacity and speed. These facts, coupled with the application of sparse matrix techniques to facilitate the inversion of large matrices, have virtually eliminated the drawbacks that at an earlier time were formidable for the Newton-Raphson method.
10
数字计算机技术最近取得了巨大的进步，特别是在存储容量和速度方面。这些事实，再加上稀疏矩阵技术的应用，以促进大矩阵的反演，几乎消除了早期牛顿-拉斐逊方法难以克服的缺点。

## Slide 11
CHAPTER 4
Methods of Solution
The Newton-Raphson method has the feature of less iterating times requirement and fast-converging. But a review of the analysis and procedures of the Newton-Raphson method of solving the power flow equations makes it evident that a significant amount of manipulation of matrices at each iteration is required.
11
牛顿-拉斐逊法具有迭代次数少、收敛速度快的特点。但是，对牛顿-拉斐逊法求解功率流方程的分析和程序的回顾表明，每次迭代都需要大量的矩阵操作。

## Slide 12
CHAPTER 4
Methods of Solution
Although this method is generally recognized as accurate and practical, it is also a fact that for transmission networks with hundreds of buses the computational aspects of the method demand considerable computing capability and computing time.
12
虽然这种方法被公认为是准确和实用的，但事实上，对于具有数百条总线的传输网络，这种方法的计算方面需要相当大的计算能力和计算时间。

## Slide 13
CHAPTER 4
Methods of Solution
Consequently, efforts have been made to uncover modified algorithms for solving the power flow equations accurately and quickly but with much less manipulation of matrices, so that results can be achieved at more reasonable levels of computer power.
13
因此，人们努力探索出精确、快速地求解潮流方程的改进算法，但对矩阵的操作要少得多，以便在更合理的计算机功率水平上获得结果。

## Slide 14
CHAPTER 4
Methods of Solution
The fast de-coupled method offers these features. Although in some cases Newton-Raphson method can get the results but the fast de-coupled method fails to converge, it does demand much less computing time and computer capacity.
14
快速去耦合方法提供了这些特性。虽然在某些情况下，牛顿-拉斐逊方法可以得到结果，但快速去耦合方法不能收敛，但它对计算时间和计算机容量的要求要小得多。

## Slide 15
谢谢聆听！
Thanks for listening！